## Slide 1: Adaptive Motor Monitoring System Based on Machine Learning Batch Training
Project Team 17
Project Instructor: Prof. Ma Chengbin
Project Sponsor: CyberInsight
Company Mentor: Fang Chen, Wentao Li
Team Members: Ting Zhang, Yiwei Cheng
Chenxin Zhou, Junru Zhu
Presented by VE450 Team 17 Nov 21. 2018
Design Review #3

## Slide 2
  Introduction
  Conceptual design
  Comprehensive analysis
  Production Plan
Contents
Presented by VE450 Team 17 Nov 21. 2018

## Slide 3
Part 1. Introduction

## Slide 4: Review of problem
- Traditional cloud one-time training of motor health monitoring system
Figure 1: cloud one-time training approach
Normal
Data Behavior
Most Recent
Data
Behavior
An industrial motor
One-time model
Compare the recent data with the one-time model
* Figure 1 from https://www.vecteezy.com/
Cloud One-time Training:
Cloud training -> low-efficiency; Easy to lose datum
One-time training -> Non-adaptive;
Cloud

## Slide 5: Needs
Edge computing
Adaptabilty to different motors
High testing accuracy
Remote control
An python-based adaptive system monitoring machine health on the edge side, with a Web UI

## Slide 6
Figure 1: cloud one-time training approach
An industrial motor
* Figure 1 from https://www.vecteezy.com/
Possible solution
- Adaptive training on the edge side to monitor motor health
Adaptive model on
Edge side
Viewable Web-UI interface
Edge adaptive Training:
Edge training -> guarantee efficiency
Adaptive training -> suitable in different circumstances

## Slide 7
Part 2. Conceptual Design

## Slide 8: Conceptual Diagram
Presentation Layer
Business Logic Layer
Figure 2: Morphological analysis of the project
Data Access Layer
An industrial motor
Raspberry Pi with an embedded algorithm(IPCA+Q)
Web UI: flask + HTML
Real-time motor data
Incremental Principle Component Analysis(IPCA)
Q-statistic
Trained data
Health Condition Value
xy vibration + rotation speed
Health Condition Value
DAQ Device
Controller
An industrial motor
Signal
Processed Signal
User

## Slide 9: Selected Design
Categories | Component | Customer Requirement
Embedded System | Raspberry Pi | Edge Computing
Algorithm | IPCA+Q ( Incremental Principal Component Analysis) SOM+MQE (Self-Organized Map) | Adapt to different motors High testing accuracy High training speed
Web User Interface | Flask + HTML | Remote Control

## Slide 10: Design Description
Raspberry Pi with Embedded Algorithm (SPCA+Q-Statistic)
Four motors
Buttons
Change condition
Demo box
User Interface
v
IPCA Algorithm
Raspberry Pi
Customer Requirement:
User Interface
Demo Box

## Slide 11: Design Description: Inside the Demo Box
Simulation Box
DAQ
DAQ: Data collection tool
Raspberry Pi: do the calculation at the edge end
Simulation Box: Simulate different conditions

## Slide 12: Design Description: Web UI
Training Process
Health Score
Threshold &Current Q

## Slide 13
Part 3. Comprehensive Analysis

## Slide 14: Validation Plan
Engineer Specification | Conduction Plan | Expected Result
Accuracy | Connect to the machine and test the false positive result | >95%
Response time | Adding the size of data and see its response according to the pressure | <200ms
Memory | Adding the size of data and see its memory condition according to pressure | <20M

## Slide 15: Validation Experiment
Train
Detect
Change Simulation Motor DataType
Re - train
Detect
1. Train the model to fit the current motor
2. Detect the motor's health condition
3. Change the motor type by altering its rotating speed
4. Detect the motor's health condition
5. Check whether the old model still fits
6. Re-train model to fit new type motor
7. Detect the motor's health condition

## Slide 16: Experiment Test Objects
Train
Detect
Change Simulation Motor DataType
Re - train
Detect
Testing Accuracy
Response Time
Training time

## Slide 17: Quantitative Results
Training batch size as 100 datums/batch works well in experiment
Memory storage: 1M
Including both datums and images in UI
For each detection period, we test 100 times using the healthy score
Only two samples report the wrong motor status => Accuracy 98%
One second is used to reach the 100% progress in training progress bar for 2000 datums.
  Training speed is 2000 datum/s
Web User Interface response time is about 200 ms tested by the web itself

## Slide 18: Analysis of Experiment Result
Categories | Component | Experiment Results | Engineering Specification
Embedded System | Raspberry Pi | Memory: 1M | Memory Required < 20M
Algorithm | IPCA+Q SOM+MQE | Testing Accuracy: 98% Training Speed: 2000 datum/s | Testing Accuracy > 95% Training Speed > 500 datum/s
Web User Interface | Flask + HTML | Response Time: 200 ms | Response Time < 200 ms

## Slide 19
Part 4. Production Plan

## Slide 20: Manufacturing Plan
Material | Quantity | Budget | Version
DAQ | 1 | 650RMB | NI USB-6008 DAQ 779051-01
Raspberry PI | 1 | 663RMB | Raspberry Pi3 B+
Server | 1 | 825RMB/year | Ali Cloud 2 core CPU, 4G cache

## Slide 21: Video

## Slide 22: Project Schedule
A
Sep 25
Oct
04
Oct 11
Oct
20
Oct
29
Nov
8
Nov
17
Nov
26
Dec 05
A
Completed
Incomplete
Checkpoint Time
B
C
E
F
D
100%
100%
Literature Research
Comparison and test
Implementation of the algorithms
Embed the algorithm into the system
Design of Web UI for a final demo
Final test
B
C
D
E
F
100%
100%
65%

## Slide 23: Reference
[1] Borah, Samarjeet, Ranjit Panigrahi, and Anindita Chakraborty. "An Enhanced Intrusion Detection System Based on Clustering." Progress in Advanced Computing and Intelligent Engineering. Springer, Singapore, 2018. 37-45.
[2] Yao, Zhewei, et al. "Hessian-based Analysis of Large Batch Training and Robustness to Adversaries." arXiv preprint arXiv:1802.08241 (2018).
[3] Robinson, Melvin D., et al. "Properties of a Batch Training Algorithm for Feedforward Networks." Neural Processing Letters 45.3 (2017): 841-854.
[4] Buczak, Anna L., and Erhan Guven. "A survey of data mining and machine learning methods for cyber security intrusion detection." IEEE Communications Surveys & Tutorials 18.2 (2016): 1153-1176.
[5] Kohonen, Teuvo. "The self-organizing map." Proceedings of the IEEE 78.9 (1990): 1464-1480.
[6] Reynolds, Douglas. "Gaussian mixture models." Encyclopedia of biometrics (2015): 827-832.
[7] Holland, Steven M. "Principal components analysis (PCA)." Department of Geology, University of Georgia, Athens, GA(2008): 30602-2501.

## Slide 24: Thank you!

## Slide 25: Q & A